## Slide 1: VLSI CAD Overview: Design, Flows, Algorithms and Tools
Konstantin Moiseev – Intel Corp. & Technion
Shmuel Wimer – Bar Ilan Univ. & Technion
Compiled from various presentation from the web.
Credits:
David Pan – Univ. of Texas Austin
Maciej Ciesielski - UMASS
Andrew Kahng – UCSD
Hai Zhou – Northwestern Univ.
Kia Bazargan – Univ. of Minnesota
Avinoam Kolodny - Technion

## Slide 2: Design Factors and Styles

## Slide 3: The Big Picture: IC Design Methods
Full Custom
ASIC – Standard Cell Design
Standard Cell
Library Design
RTL-Level Design
Design Methods
Cost / Development
Time
Quality
# Companies involved
Notes: What is the difference between full custom and ASIC design?
Tools used in Full Custom would be Magic-like, and tools used in RTL-Level Design would be CAD tools for synthesis, physical design, etc.
Since Full Custom costly (number of designers, design time, fabrication cost, scalability, etc.) only companies like Intel afford
This course will cover the underlying theory for the tools that are used mostly in the last two methods.

## Slide 4: Optimization: Levels of Abstraction
Algorithmic
  Encoding data, computation scheduling, balancing delays of components, etc.
Gate-level
  Reduce fan-out, capacitance
  Gate duplication, buffer insertion
Layout / Physical-Design
  Move cells/gates around to shorten wires on critical paths
  Abut rows to share power / ground lines
Effectiveness
Level of details

## Slide 5: Full Custom

## Slide 6: Full Custom

## Slide 7: Standard Cell (Semi Custom)

## Slide 8: Cell-Based Design (Standard Cells)
Routing channel
requirements are
reduced by presence
of more interconnect
layers

## Slide 9: FPGA: Lookup Table (LUT)
Look-up Table
  Truth table implemented in hardware
  Can implement arbitrary function with fixed number of inputs (typically 4-5) by programming the storage bits (customizing the truth table)
F = x1’x2’ + x1x2
x1 x2 F
0 0 1
0 1 0
1 0 0
1 1 1
2-Input LUT
0/1
x1 x2
0/1
0/1
0/1
F
1
0
0
1
Programming bit P

## Slide 10: FPGA: Logic Element
Logic Element: the basic programmable element of FPGA
  Contains LUT
Programming is a domain of specialized technology mapping onto device specific structure
Look-Up
Table
(LUT)
State
Out
Inputs
Clock
Enable

## Slide 11: FPGA: Architecture
Each programmable logic element outputs one data bit
Interconnects are also programmable
A domain of physical synthesis (place and route)
LE
LE
LE
LE
LE
LE
LE
LE
LE
LE
LE
LE
Logic Element
Tracks

## Slide 12: FPGA: Architecture

## Slide 13: Comparison of Design Styles
style

## Slide 14: Comparison of Design Styles
Area
Performance
Fabrication layers
style
full-custom
standard cell
gate array
FPGA
compact
high
compact
to moderate
moderate
large
high
to moderate
moderate
low
ALL
ALL
routing layers
none

## Slide 15: Comparison of Design Styles

## Slide 16: Design Styles Tradeoffs

## Slide 17: The Inverted Pyramid (~2000)
Electronic Systems > $1 Trillion
Semiconductor > $220 B
CAD $3 B

## Slide 18: Moore’s law
Moore’s law – exponential growth in complexity
1 billion transistors
Notes: Explain why design went multicore and what are main limitations (power, complexity, interconnect)

## Slide 19: Data explosion and productivity
Notes: Emphasis on physical design

## Slide 20: Evolution of the EDA Industry
Results
(design productivity)
Effort (EDA tool effort)
Transistor entry – Calma, Computervision, Magic
Schematic entry – Daisy, Mentor, Valid
Synthesis – Cadence, Synopsys
What’s next?

## Slide 21: History of VLSI Layout Tools

## Slide 22: Synthesis and Design Process (High Level)
Application (graphics, DSP, general processor)
Algorithm (Z-buffer, FFT)
Architecture (pipeline, cash sharing, parallelism)
High level synthesis
Logic and physical synthesis

## Slide 23: VLSI Design Flow
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
Chip Planning
Placement
Signal Routing
Partitioning
Timing Closure
Clock Tree Synthesis

## Slide 24: High Level Synthesis (HLS)
Converting high-level design description to RTL
Input:
  High-level languages (C, system C, system Verilog)
  Hardware description languages (Verilog, VHDL)
  State diagrams / logic networks
Tools:
  Parser, compiler
  Library of modules
Constraints:
  Resource constraints (number of modules of a certain type)
  Timing constraints (latency, delay, clock cycle)
Output:
  Operation scheduling (time) and binding (resource)
  Control generation
  RTL architecture

## Slide 25: Design Compilation
Lex
Parse
Compilation front-end
Behavioral Optimization
Intermediate form
Arch synth
Logic synth
Lib Binding
HLS backend
Separation into
Data Path (arithmetic)
Control (Boolean logic)

## Slide 26: Behavioral Optimization
Techniques used in software compilation
  Expression tree height reduction
  Constant and variable propagation
  Common sub-expression elimination
  Dead-code elimination
  Operator strength reduction (e.g., *4  << 2)
Hardware transformations
  Conditional expansion
    If c then x = A
    else x = B;
    Compute A and B in parallel: x = C ? A : B (MUX)
  Loop unrolling
    Replace k iterations of a loop by k instances of the loop body
A
B
x
c
x = a + b  c + d

+
+
a
b
c
d
+
+

a
d
b
c

## Slide 27: Data Flow Graph Transformation
x
+
a
b
c
F
F = a*b + a*c
F = a*(b + c)
Transformation
+
x
a
b
c
x
F

## Slide 28: Optimization in Temporal Domain
Scheduling
Mapping of operations to time slots (cycles)
Uses sequencing graph (data flow graph, DFG)
Goal: minimize latency (s.t. resource constraints)
+
NOP






+
<
-
-
NOP
1
2
3
4
+
NOP






+
<
-
-
NOP
1
2
3
4

## Slide 29: Optimization in Spatial Domain
Resource allocation & binding
Assigning operations to hardware units
Allocating registers
Binding operations to same resource
Goal: minimize resource (s.t. latency constraints)
+
NOP






+
<
-
-
NOP
1
2
3
4

## Slide 30: Synthesis Flow at Logic Level
module example(clk, a, b, c, d, f, g, h)
input clk, a, b, c, d, e, f;
output g, h; reg g, h;
always @(posedge clk) begin
g = a | b;
if (d) begin
if (c) h = a&~h;
else h = b;
if (f) g = c; else a^b;
end else
if (c) h = 1; else h ^b;
end
endmodule
Specification
d
a
b
e
f
c
0
h
g
clk
Logic Extraction
a multi-stage process
Technology-Independent Optimization
f
g0
h1
a
c
e
g1
h3
h5
H
G
b
d
Technology-Dependent Mapping
f
d
b
e
a
c
clk
h
H
G
g
Physical Synthesis

## Slide 31: Logic Optimization Methods
Logic Optimization
Multi-level logic
(standard cells)
Two-level logic (PLA)
Exact (QM)
Heuristic
(espresso)
Structural
(SIS,ABC)
Functional
(AC, Kurtis)
Functional
(BDD-based)
algebraic
Boolean
Boolean
Depends on target technology

## Slide 32: Optimization Criteria for Synthesis
Area occupied by the logic gates and interconnect (approximated by literals = transistors in technology independent optimization)
Critical path delay of the longest path through logic
Degree of testability of the circuit
Power consumed by the logic gates
Placeability, Wireability

## Slide 33: Transformation-Based Synthesis
sequence of transformations that change network topology and its characteristics
All modern synthesis systems are built that way
  work on uniform network representation
  use scripts, lists of transformations forming a strategy
Transformations are mostly algebraic
  very little is based on Boolean factorization
Representation
  Cube notation, BDDs, AIGs
The underlying algorithms
  Algebraic transformations
  Collapsing, decomposition
  Factorization, substitution

## Slide 34: Multi-Level Logic Minimization
Objective
  Minimize number of literals
  Literals represent inputs to CMOS gates
Representation
  Factored form
  Compatible with CMOS
Optimization techniques
  Algebraic factorization and decomposition (heuristic)
    Technology independent
  Requires mapping onto target architecture
    Standard cells
    FPGAs (LUT)

## Slide 35: Two-Level Logic Minimization
Representation
Truth tables
Karnaugh maps
Sum of Products (SOP) form
Binary Decision Diagrams (BDD)
Objective
Minimize number of product terms in SOP
Challenge: multiple-output functions
Optimization techniques
Quine McCluskey (optimal)
Espresso logic minimizer (heuristic)
Ashenhust-Curtis functional decomposition (nearly optimal)
BDD-based (heuristic)

## Slide 36: Physical Design Steps
Circuit partitioning
Floorplanning
Pin assignment
Placement
Routing
Convergence

## Slide 37: Partitioning
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
Chip Planning
Placement
Signal Routing
Partitioning
Timing Closure
Clock Tree Synthesis

## Slide 38: Partitioning
Circuit:
Cut ca: four external connections
1
2
4
5
3
6
7
8
5
6
4
8
7
2
3
1
5
6
4
8
7
2
3
1
Cut ca
Cut cb
Block A
Block B
Block A
Block B
Cut cb: two external connections

## Slide 39: Partitioning - optimization Goals
In detail, what are the optimization goals?
  Number of connections between partitions is minimized
  Each partition meets all design constraints (size, number of external connections..)
  Balance every partition as well as possible
How can we meet those goals?
  Unfortunately, this problem is NP-hard
  Efficient heuristics developed in the 1970s and 1980s. High quality and low-order polynomial time.
39

## Slide 40: Floorplanning
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
Chip Planning
Placement
Signal Routing
Partitioning
Timing Closure
Clock Tree Synthesis

## Slide 41: Floorplanning
GND
VDD
Module e
I/O Pads
Block Pins
Block a
Block b
Block d
Block e
Floorplan
Module d
Module c
Module b
Module a
Chip Planning
Block c
Supply Network
© 2011 Springer Verlag

## Slide 42: Floorplanning
Example
Given: Three blocks with the following potential widths and heights
Block A: w = 1, h = 4 or w = 4, h = 1 or w = 2, h = 2
Block B: w = 1, h = 2 or w = 2, h = 1
Block C: w = 1, h = 3 or w = 3, h = 1
Task: Floorplan with minimum total area enclosed
A
A
A
B
B
C
C

## Slide 43: Floorplanning
Example
Given: Three blocks with the following potential widths and heights
Block A: w = 1, h = 4 or w = 4, h = 1 or w = 2, h = 2
Block B: w = 1, h = 2 or w = 2, h = 1
Block C: w = 1, h = 3 or w = 3, h = 1
Task: Floorplan with minimum total area enclosed

## Slide 44: Floorplanning
Solution:
Aspect ratios Block A with w = 2, h = 2; Block B with w = 2, h = 1; Block C with w = 1, h = 3
This floorplan has a global bounding box with minimum possible area (9 square units).
Example
Given: Three blocks with the following potential widths and heights
Block A: w = 1, h = 4 or w = 4, h = 1 or w = 2, h = 2
Block B: w = 1, h = 2 or w = 2, h = 1
Block C: w = 1, h = 3 or w = 3, h = 1
Task: Floorplan with minimum total area enclosed

## Slide 45: Placement
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
Chip Planning
Placement
Signal Routing
Partitioning
Timing Closure
Clock Tree Synthesis

## Slide 46: Placement
© 2011 Springer Verlag
c
h
f
b
a
g
d
e
a
c
b
h
g
d
e
f
e
h
g
f
d
a
c
b
GND
VDD
Linear Placement
2D Placement
Placement and Routing with Standard Cells
h
e
d
a
g
f
c
b

## Slide 47: Placement
Global Placement
Detailed Placement

## Slide 48: Placement Optimization Objectives
Total Wirelength
Number of Cut Nets
Wire Congestion
Signal Delay
© 2011 Springer Verlag

## Slide 49: Routing
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
Chip Planning
Placement
Signal Routing
Partitioning
Timing Closure
Clock Tree Synthesis

## Slide 50: Routing
Given a placement, a netlist and technology information,
determine the necessary wiring, e.g., net topologies and specific routing segments, to connect the cells
while respecting constraints, e.g., design rules and routing resource capacities, and
optimizing routing objectives, e.g., minimizing total wirelength and maximizing timing slack.

## Slide 51: Routing
C
D
A
B
4
3
2
1
4
3
4
1
1
6
5
4
Netlist:
N1 = {C4, D6, B3}
N2 = {D4, B4, C1, A4}
N3 = {C2, D5}
N4 = {B1, A1, C3}
Technology Information (Design Rules)
Placement result

## Slide 52: Routing
Netlist:
N1 = {C4, D6, B3}
N2 = {D4, B4, C1, A4}
N3 = {C2, D5}
N4 = {B1, A1, C3}
Technology Information (Design Rules)
C
D
A
B
4
3
2
1
4
3
4
1
1
6
5
4
N1

## Slide 53: Routing
Netlist:
N1 = {C4, D6, B3}
N2 = {D4, B4, C1, A4}
N3 = {C2, D5}
N4 = {B1, A1, C3}
Technology Information (Design Rules)
C
D
A
B
4
3
2
1
4
3
4
1
1
6
5
4
N2
N3
N4
N1

## Slide 54: The Design Closure Problem
Iterative removal of timing violations (white lines)

## Slide 55: Design Verification
Ensuring correctness of the design against its implementation (at different levels)
behavior
structure
function
layout
HDL / RTL
Gate level
Logic level
Mask level
Design
 ?
 ?
 ?
model
 ?

## Slide 56: Algorithm Design Techniques
Greedy
Divide and Conquer
Dynamic Programming
Network Flow
Mathematical Programming (e.g., linear programming, integer linear programming)

## Slide 57: Reduction
Idea: If I can solve problem A, and if problem B can be transformed into an instance of problem A, then I can solve problem B by reducing problem B to problem A and then solve the corresponding problem A.
Example:
  Problem A: Sorting
  Problem B: Given n numbers, find the i-th largest numbers.
Notes: “How to solve it” – george polya(Hungarian)

## Slide 58: Analysis of Algorithm
There can be many different algorithms to solve the same problem.
Need some way to compare 2 algorithms.
Usually run time is the most important criterion used
  Space (memory) usage is of less concern now
However, difficult to compare since algorithms may be implemented in different machines, use different languages, etc.
Also, run time is input-dependent. Which input to use?
Big-O notation is widely used for asymptotic analysis.