## Slide 1
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
Chip Planning
Placement
Signal Routing
Partitioning
Timing Closure
Clock Tree Synthesis

## Slide 2
Introduction to Floorplanning
Optimization Goals in Floorplanning
Floorplan Representations
Floorplanning Algorithms
Floorplan Sizing
Outline

## Slide 3
GND
VDD
Module e
I/O Pads
Block Pins
Block a
Block b
Block d
Block e
Floorplan
Module d
Module c
Module b
Module a
Chip Planning
Block c
Supply Network

## Slide 6
Example
Given: Three blocks with the following potential widths and heights
Block A: w = 1, h = 4 or w = 4, h = 1 or w = 2, h = 2
Block B: w = 1, h = 2 or w = 2, h = 1
Block C: w = 1, h = 3 or w = 3, h = 1
Task: Floorplan with minimum total area enclosed
A
A
A
B
B
C
C

## Slide 7
Example
Given: Three blocks with the following potential widths and heights
Block A: w = 1, h = 4 or w = 4, h = 1 or w = 2, h = 2
Block B: w = 1, h = 2 or w = 2, h = 1
Block C: w = 1, h = 3 or w = 3, h = 1
Task: Floorplan with minimum total area enclosed

## Slide 8
Solution:
Aspect ratios Block A with w = 2, h = 2; Block B with w = 2, h = 1; Block C with w = 1, h = 3
This floorplan has a global bounding box with minimum possible area (9 square units).
Example
Given: Three blocks with the following potential widths and heights
Block A: w = 1, h = 4 or w = 4, h = 1 or w = 2, h = 2
Block B: w = 1, h = 2 or w = 2, h = 1
Block C: w = 1, h = 3 or w = 3, h = 1
Task: Floorplan with minimum total area enclosed

## Slide 9
Area and shape of the global bounding box
  Global bounding box of a floorplan is the minimum axis-aligned rectangle that contains all floorplan blocks.
  Area of the global bounding box represents the area of the top-level floorplan
  Minimizing the area involves finding (x,y) locations, as well as shapes, of the individual blocks.
Total wire length
  Long connections between blocks may increase signal propagation delays in the design.

## Slide 10
Combination of area area(F) and total wire length L(F) of floorplan F
  Minimize α ∙ area(F) + (1 – α) ∙ L(F) where the parameter 0 ≤ α ≤ 1 gives the relative importance between area(F) and L(F)
Signal delays
  Static timing analysis is used to identify the interconnects that lie on critical paths.

## Slide 11
A rectangular dissection is a division of the chip area into a set of blocks or non-overlapping rectangles.
A slicing floorplan is a rectangular dissection
  Obtained by repeatedly dividing each rectangle, starting with the entire chip area, into two smaller rectangles
  Horizontal or vertical cut line.
A slicing tree or slicing floorplan tree is a binary tree with k leaves and k – 1 internal nodes
  Each leaf represents a block
  Each internal node represents a horizontal or vertical cut line.

## Slide 12
Slicing floorplan and two possible corresponding slicing trees
b
d
a
e
c
f
a
c
b
d
e
f
H
V
H
H
V
H
V
H
d
c
e
f
H
V
b
a

## Slide 13
Non-slicing floorplans (wheels)
b
d
a
e
c
a
b
c
d
e

## Slide 14
Floorplan tree: Tree that represents a hierarchical floorplan
a
b
c
d
e
f
g
h
i
H
H
H
H
V
W
h
i
c
d
e
f
g
a
b
H
H
Horizontal division (objects to the top and bottom)
H
V
Vertical division (objects to the left and right)
H
W
Wheel (4 objects cycled around a center object)

## Slide 15: Floorplan and Layout
Floorplan
Graph representation
B2
B1
B3
B5
B4
B6
B12
B9
B8
B7
B10
B11
B2
B1
B10
B5
B12
B6
B3
B9
B8
B7
B11
B4
Vertices - vertical lines. Arcs - rectangular areas where blocks are embedded.
Floorplan is represented by a planar graph.
A dual graph is implied.

## Slide 16: From Floorplan to Layout
Actual layout is obtained by embedding real blocks into floorplan cells.
  Blocks’ adjacency relations are maintained
  Blocks are not perfectly matched, thus white area (waste) results
Layout width and height are obtained by assigning blocks’ dimensions to corresponding arcs.
  Width and height are derived from longest paths
Different block sizes yield different layout area, even if block sizes are area invariant.

## Slide 17: Area Minimization of Slicing Floorplan
h
h
v
v
v
v
B2
B1
B3
B5
B4
B6
B11
B3
B4
B5
B6
B8
B9
B10
B1
B2
B7
h
h
h
h
B12
B12
B9
B8
B7
B10
B11
Slicing tree. Leaf blocks are associated with areas.
v
Top block’s area is divided by vertical and horizontal cut-lines

## Slide 19
+
=
+
=
+
=
Merge horizontally two width-height sets (vertical cut-line)
v

## Slide 20
h
Size of new width-height list equals sum of lengths of children lists, rather than their product.

## Slide 21: Sketch of Proof
Problem is solved by a bottom-up dynamic programming algorithm working on corresponding slicing tree.
Each node maintains a set of width-height pairs, none of which can be ruled out until root of tree is reached. Size of sets is in the order of node’s leaf count. Sets in leaves are just Bi’s two orientations.

## Slide 22: Sketch of Proof
The sets of width-height pairs at each node is created by merging the sets of left-son and right-son sub-trees in time linear in their size.
Width-height pair sets are maintained as a sorted list in one dimension (hence sorted inversely in the other dimension).
Final implementation is obtained by backtracking from the root.

## Slide 23
Shape functions
Legal shapes
Legal shapes
w
h
w
h
Block with minimum width and height restrictions
ha*aw  A

## Slide 24
Shape functions
w
h
Hard library block
w
Discrete (h,w) values

## Slide 25
Corner points
5
2
2
5
2
5
2
5
w
h

## Slide 26
Algorithm
This algorithm finds the minimum floorplan area for a given slicing floorplan in
polynomial time. For non-slicing floorplans, the problem is NP-hard.
Construct the shape functions of all individual blocks
Bottom up: Determine the shape function of the top-level floorplan from the shape functions of the individual blocks
Top down: From the corner point that corresponds to the minimum top-level floorplan area, trace back to each block’s shape function to find that block’s dimensions and location.

## Slide 27
4
2
2
4
Block B:
Block A:
5
5
3
3
Step 1: Construct the shape functions of the blocks

## Slide 28
4
2
2
4
Block B:
Block A:
5
5
3
3
Step 1: Construct the shape functions of the blocks
2
4
h
6
w
2
6
4
5
3

## Slide 29
4
2
2
4
Block B:
Block A:
5
5
3
3
Step 1: Construct the shape functions of the blocks
2
4
h
w
2
6
4
6
3
5

## Slide 30
4
2
2
4
Block B:
Block A:
5
5
3
3
w
2
6
2
4
h
4
6
hA(w)
Step 1: Construct the shape functions of the blocks

## Slide 31
4
2
2
4
Block B:
Block A:
5
5
3
3
hB(w)
w
2
6
2
4
h
4
6
hA(w)
Step 1: Construct the shape functions of the blocks

## Slide 32
w
2
6
2
4
h
4
6
hB(w)
hA(w)
8
w
2
6
2
4
h
4
6
hB(w)
hA(w)
hC(w)
8
Step 2: Determine the shape function of the top-level floorplan (vertical)

## Slide 33
w
2
6
2
4
h
4
6
w
2
6
2
4
h
4
6
hB(w)
hA(w)
hB(w)
hA(w)
hC(w)
3 x 9
4 x 7
5 x 5
8
8
Minimimum top-level floorplan
with vertical composition
Step 2: Determine the shape function of the top-level floorplan (vertical)

## Slide 34
2 x 4
3 x 5
5 x 5
Step 3: Find the individual blocks’ dimensions and locations
w
2
6
2
4
h
4
6
(1) Minimum area floorplan: 5 x 5
(2) Derived block dimensions : 2 x 4 and 3 x 5
8
Horizontal composition